## Slide 1: ROBOTICS 2
Dynamic identification of robot dynamics from motor torques w/o signs
Final Project
Marco Pennese
Veronica Vulcano
A.Y. 2019/2020

## Slide 2: PBPR ALGORITHM INTRODUCTION 01 02 ESTIMATING SIGNS: TREE ALGORITHM 03 RESULTS 04
Results of the experiments on 1R and 3R robot
Torque sign estimation
Dynamic Identification of Robot Parameters
Description of the project
05
EXTENSION
Extension of the algorithm to a real robot (Franka Emika Panda)

## Slide 3
The goal of our work is to perform the dynamic identification of a robot, estimating its
dynamic parameters/coefficients by solving an optimization problem.
We have dealt with the problem of torque sign lack, as in some real robot (e.g. KUKA KR5),
in which we can't use traditional methods for dynamic identification.
For this reason, we have developed an algorithm able to estimate torque signs so that
we could proceed with the identification using well known strategies.
We first studied a simple 1R robot under gravity; then, we moved to a more complex robot,
a 3R spatial robot.
INTRODUCTION

## Slide 4
Penalty
Based
Parameters
Retrieval
Algorithm
We need to solve the following optimization problem:
In order to get a physically consistent set of parameters, the term takes into account the violation of physical constraints such as:
triangular inequalities for inertia tensors;
the total sum of the link masses must be in the boundaries.
The quantities and can always be defined based on a priori knowledge.

## Slide 5: PROBLEM!
We cannot apply directly the PBPR algorithm because we are supposed to not to know the torque sign information, while the algorithm needs it.
So, we should devise a strategy to estimate the torque signs from what we have.
?

## Slide 6: ESTIMATING SIGNS

## Slide 7: ESTIMATING SIGNS

## Slide 8: ESTIMATING SIGNS

## Slide 9: ESTIMATING SIGNS

## Slide 10: ESTIMATING SIGNS
segment 1
segment 2
segment 3
segment 4
segment 5

## Slide 11
We would like to treat each segment independently.
ESTIMATING SIGNS
We can group rows that refer to the same segment in the same block.
So, for the -th segment the problem becomes:

## Slide 12
=
We would like to treat each segment independently also when they belong to different joint torques and they could possibly be simultaneous.

## Slide 13
=
Each segment is independent!

## Slide 14
ESTIMATING SIGNS
2 possibilities:
We expect that when we solve the problem with the wrong sign, the value of is larger.
For each segment we can solve the sequent problem by using the PBPR algorithm.

## Slide 15: BUILDING THE TREE
+
+ +
+ -
+ - +
+ - -
+ + -
+ + +
-
- +
- -
- - +
- - -
- + -
- + +
. . .
If we analyse the segments in order, we will obtain the sequent tree:
segment 1
segments 1 and 2
segments 1, 2 and 3
The problem is exponential: with segments, we will have possible solutions!

## Slide 16: PRUNING THE TREE
+
-
segment 1
We need a strategy to expand only promising branches:
We expanded only the best branches (with the lower loss).

## Slide 17: PRUNING THE TREE
+
+ +
+ -
-
- +
- -
segment 1
segments 1 and 2
We need a strategy to expand only promising branches:
with

## Slide 18: PRUNING THE TREE
+
+ +
+ -
+ - +
+ - -
+ + -
+ + +
-
- +
- -
- - +
- - -
. . .
segment 1
segments 1 and 2
segments 1, 2 and 3
We need a strategy to expand only promising branches:
In our experiments we chose

## Slide 19
MAKING THE PROBLEM WELL-CONDITIONED
By taking the segments independently, it may be the case in which has not full rank. So, we need something to deal with this possibility and always have well defined problems.
First, we need to find a problem that is well-defined. We define a threshold and find a minimal set of segments for which the condition number of the corresponding is under the threshold.
Then we proceed by analysing the segments in the order that minimize the condition number.

## Slide 20
MAKING THE PROBLEM WELL-CONDITIONED
Let’s suppose that we found a set of 3 segments yielding a well-defined problem.
+ - +
+ - -
+ + -
+ + +
- - +
- - -
- + -
- + +
+ + - +
+ + - -
+ - + +
+ - + -
- + - +
- + - -
+ + - + +
+ + - + -
+ + - - +
+ + - - -
+ - + - +
+ - + - -
…
+ + -
+ - +
- + -
The next segment is the one that added to the others minimizes the condition number.

## Slide 21
+ | - | - | + | - | + | +
PBPR
Algorithm
physically consistent dynamic parameters
Forward pruning ();
Make the problem well-conditioned;
Pattern search;
Best combination of signs (with the lowest loss)
Simulated annealing
SUMMARIZING

## Slide 22: RESULTS
Experiments on 1R and 3R robot

## Slide 23
1R ROBOT UNDER GRAVITY
Dynamic Model

## Slide 24
1R ROBOT UNDER GRAVITY
Experiment 1
Coefficients error is:

## Slide 25
1R ROBOT UNDER GRAVITY
Experiment 2
Coefficients error is:

## Slide 26
1R ROBOT UNDER GRAVITY
Experiment 3
Coefficients error is:
We chose and

## Slide 27
1R ROBOT UNDER GRAVITY
Validation

## Slide 28
3R SPATIAL ROBOT
Dynamic Model
The dynamic coefficients we found are:

## Slide 29
3R SPATIAL ROBOT
Experiment 1

## Slide 30
3R SPATIAL ROBOT
Experiment 1
Coefficients error is:

## Slide 31
3R SPATIAL ROBOT
Experiment 2

## Slide 32
3R SPATIAL ROBOT
Experiment 2
Coefficients error is:

## Slide 33
3R SPATIAL ROBOT
Validation

## Slide 34: CONSIDERATIONS
PRO:
The pruning of the tree drastically increases the velocity of the algorithm and it is worth the risk of discarding some good solutions;
In every instant of time the algorithm deals with physically consistent hypothesis;
DRAWBACKS:
With forward pruning we run the risk of discarding branches that might lead to an optimal solution, but we can realize it during the validation phase and run again the algorithm with different parameters.
We discard under-threshold samples (which are at least 10% of the total); too short segments are discarded too; since these samples are near to zero, we can imagine that they are poorly informative.
A possible problem is when the threshold is not correctly identified, but this seldom happens, and it could be solved simply by choosing a bigger threshold;
The algorithm becomes slower and slower as the robot complexity increases!

## Slide 35
EXTENSION
As before, we proceeded by taking the absolute value of the torque, so to pretend that we didn't have this kind of information. At this stage we could apply our tree algorithm to estimate the signs.
By doing so, we faced a big problem: in fact, when the robot increases its complexity, the tree algorithm becomes tremendously slow and it takes days or even weeks to finish its execution.
Applying the Algorithm to a real Robot:
Franka Emika Panda
* Dynamic Identification of the Franka Emika Panda Robot with Retrieval of Feasible Parameters using Penalty Based Optimization (Gaz, Cognetti, Oliva, Giordano, De Luca)

## Slide 36: RELAXING THE PROBLEM
Being unable to use the algorithm as it is, we tried to relax some constraint while solving the optimization problems of the tree.
By ignoring the constraints that ensure us physically consistent parameters we can re-write the optimization problem in the following form:
And we can find the solution in closed form as:
where is the pseudoinverse of

## Slide 37
Using this relaxed problem in the tree, and not checking for the physical meaning of each term, we end up with 2 best solutions: one the opposite of the other.
and
Of course only one of the two is physically consistent, and we don't know a priori which is of the two.
+ | - | - | + | - | + | +
- | + | + | - | + | - | -
2 possibilities
PBPR
Algorithm
choose the best by comparing the two losses
+ | - | - | + | - | + | +
Best signs combination +
related physically consistent dynamic parameters
The execution is much faster:
~10min for estimating the signs + the time to run 2 times the PBPR algorithm

## Slide 38
FRANKA EMIKA PANDA
Results
Correctly predicted signs:
105/105
Coefficients error is:

## Slide 39
FURTHER EXPANSIONS
The algorithm works quite well in all the cases that we studied
We could estimate the threshold in a more smart way (e.g. taking into account the derivatives of the torque)
The next step of the project could be to apply the sign estimation, using the tree algorithm, to a real robot that outputs only the absolute value of the torque (like the KUKA KR5) and try to detect the dynamic parameters of such a robot

## Slide 40
THANK YOU
FOR YOUR ATTENTION!